## Slide 1: RNA-seq data analysis Matt Settles, PhD University of California, Davis settles@ucdavis.edu
Workshop
ESALQ-USP, Piracicaba, SP
July 17th to July 19th, 2015 (8:30AM-6:00PM)

## Slide 2: Outline
Introduction to High Throughput Sequencing and RNA-seq
  High throughput sequencing
  RNA-seq Experimental Design
  RNA Sequencing and Sample Preparation
Overview of RNA-seq Data Analysis
  Pipeline Workflow/Stages
  Software
  Metadata input
  Files and Directory Structure
Workshop Dataset
Introduction to the Command Line

## Slide 3: outline
Read Preprocessing
  Description of the expHTS preprocess pipeline
  Parameters and what they mean
  Preprocessing the Workshop Data
  QA/QC
Read Mapping
  Description of the expHTS mapping pipeline
  Parameters and what they mean
  Mapping the Workshop Data
  QA/QC
Estimate known genes and transcripts expression – Counting
  Description of the expHTS counting pipeline
  Parameters and what they mean
  Counting the Workshop Data
  QA/QC

## Slide 4: Outline
Differential Expression Analysis using edgeR
  Overview of Differential Expression Analysis
  Models and model formulation
  QA/QC
  Perform Differential Expression the Workshop Data
Summarization and Visualization of Output

## Slide 5: Introduction to sequencing
Section 1

## Slide 6: History
It would take a few more decades after the discovery of the double helix in 1953 before we could readily analyze fragments of DNA.
RNA sequencing actually preceded DNA sequencing when Walter Friers from the University of Ghent published the first complete gene and genome of Bacteriophage MS2 in 1972 and 1976 respectively.
Location specific primer extension: Raw Wu (1970), using DNA polymerase catalysis and specific nucleotide labeling.
Chain-terminating inhibitors: Frederick Sanger (1977), aided in speeding up the process

## Slide 7: history
Leroy E. Hood’s laboratory at the California Institute of Technology announced the first semi-automated DNA sequencing machine in 1986.
Applied Biosystems’ produced the first fully automated sequencing machine, the ABI 370, in 1987, followed by the ABI Prism 373, (1990), ABI Prism 377 (1995), ABI Prism 310 (also 1995) represented the first capillary sequencer, ABI Prism 3700 (1999, the workhorse of the human genome project), ABI 3730xl DNA analyzer (2002) @ 2M bases per day.

## Slide 8
Primer Walking
  Design a primer that matches the sequence neighboring the unknown sequence
  Sequence the short DNA strand using the Sanger method
  The new sequenced portion is used to design a new primer and repeated
de novo sequencing or “shotgun sequencing”
  High-molecular weight DNA is sheared into random
  fragments
  Shorter fragments are cloned into a vectors
  clones are sequenced from both ends, creating two ”reads”
  original sequence is reconstitutes by ”assembling” the reads

## Slide 9: Sequencing Costs
April – 2015
  $0.05 per Megabase
  $4,211 per Human Sized Genome (30x coverage)
GROWTH IN SEQUENCING

## Slide 10: Roche 454
The first massively parallel method to become commercially available was developed by 454 Life Sciences in 2005 (acquired by Roche in 2007) and is based on the pyrosequencing technique. Similar to the Sanger method, sequencing is carried out using primed synthesis by DNA polymerase. However in the 454 pyrosequencing method, the DNA fragments are presented with each of the four dNTPs sequentially and without a dye-terminator, as is done with Sanger sequencing, allowing for multiple incorporation in the same flow. The amount of the incorporation is monitored by luminometric detection of the pyrophosphate released (hence the name ”pyrosequencing”).

## Slide 11: Illumina (SOLEXA)
The second next-generation sequencing technology to be released (in 2006) was Illumina Solexa sequencing. A key difference between Roche 454 and Illumina sequencing was the use of chain-terminating nucleotides. The fluorescent label on the terminating base can be removed to leave an unblocked 3’ terminus, mating the chain termination a reversible process. The method thus sequences one base at a time, rather than 0 or more bases as does Roche 454.
Illumina SBS

## Slide 12: Life Technologies
Ion Torrent PGM, first available in 2011, generates up to 400bp reads (reported) and up to 2Gb (5.5m reads) per run. Cheap fast runs. Ion Proton system can generate up to 10Gb per run. Generates flowgrams and SFF files similar to Roche 454 data as well as the standard fastq files.

## Slide 13: Pacific Biosystems
Pacific Biosystems is so far the most successful third generation DNA sequencing system. Key differences are that its a single molecule, real time (SMRT) technology and capable of producing sequences of multi-kilobases.

## Slide 14: Oxford nanopore
Announced in 2012, Oxford Nanopore sent a ripple through the sequencing community but has yet to live up to expectations. Promises ”tens of kbs”.

## Slide 15: Experimental design
In high throughput biological work (Microarrays, Sequencing, HT Genotyping, etc.), what may seem like small technical artifacts introduced during sample extraction/preparation can lead to large changes, or technical bias, in the data.
  Not to say this doesn’t occur with smaller scale analysis such as Sanger sequencing or qRT-PCR, but they do become more apparent and may cause significant issues during analysis.

## Slide 16: General rules for preparing samples
Prepare more samples then you are going to need, i.e. expect some will be of poor quality, or fail
Preparation stages should occur across all samples at the same time (or as close as possible) and by the same person
Spend time practicing a new technique to produce the highest quality product you can, reliably
Quality and quantity should be established using Fragment analysis traces (pseudo-gel images)
DNA/RNA should not be degraded
  260/280 ratios for RNA should be approximately 2.0 and 260/230 should be between 2.0 and 2.2. Values over 1.8 are acceptable
BE CONSISTENT ACROSS ALL SAMPLES!!!

## Slide 17: Sequencing Depth
The first and most basic question is how many base pairs of sequence data will I get Factors to consider are:
1. Number of reads being sequenced 2. Read length (if paired consider then as individuals) 3. Number of samples being sequenced 4. Expected percentage of usable data
The number of reads and read length data are best obtained from the manufacturer’s website (search for specifications) and always use the lower end of the estimate.

## Slide 18: Sequencing Coverage
Once you have the number of base pairs per sample you can then determine expected coverage Factors to consider are:
1. Length of the genome (in bp) 2. Any extra-genomic sequence, or contamination
Coverage is counted differently for ”Counting” based experiments (RNAseq, amplicons) where an expected number of reads per sample is sometimes more suitable.

## Slide 19: RNA-seq
Characterization of transcripts or differential gene expression
Factors to consider are:
Read length needed depends on likelihood of mapping uniqueness, but generally longer is better and paired-end is better than single-end. (2 x >75bp is recommended)
Interest in measuring genes expressed at low levels ( << level, the >> the depth and necessary complexity of library)
The fold change you want to be able to detect ( < fold change more replicates, more depth)
Detection of novel transcripts, or quantification of isoforms requires >> sequencing depth
The amount of sequencing needed for a given sample is determined by the goals of the experiment and the nature of the RNA sample.

## Slide 20: Generating RNA-seq libraries
Considerations
QA/QC of RNA samples
RNA of interest
Library Preparation
  Stranded vs Unstranded
Size Selection/Cleanup
  Final QA

## Slide 21: QA/QC of RNA samples
RNA Quality and RIN (RQN on AATI Fragment Analyzer)
RNA sequencing begins with high-quality total RNA, only an Agilant BioAnalyzer (or equivalent) can adequately determine the quality of total RNA samples. RIN values between 7 and 10 are desirable.
BE CONSISTANT!!!

## Slide 22: RNA of interest
From total RNA we extract ”RNA of interest”. Primary goal is to NOT sequence 90% (or more) ribosomal RNAs, which are the most abundant RNAs in the typical sample. there are two main strategies for enriching your ”RNA of interest”.
  polyA selection. Enrich mRNA (those with polyA tails) from the sample by oligo dT affinity.
  rRNA depletion. rRNA knockdown using RiboZero (or Ribominus) is mainly used when your experiment calls for sequencing non-polyA RNA transcripts and non-coding RNA (ncRNA) populations. This method is also usually more costly.
rRNA depletion will result in a much larger proportion of reads align to intergenic and intronic regions of the genome.

## Slide 23: Library Preparation
Most library prep methods first require you to generate cDNA, in order to ligate on the Illumina barcodes and adapters.
  cDNA generation using oligo dT (3’ biased transcripts)
  cDNA generation using random hexomers (less biased)
  full-length cDNAs using SMART cDNA synthesis method
Also, can generate strand specific libraries, which means you only sequence the strand that was transcribed.
  This is most commonly performed using dUDP rather than dNTPs in cDNA generation and digesting the “rna” strand.
  Can also use a RNA ligase to attach adapters and then PCR the second strand and remainder of adapters.

## Slide 24: Size Selection/Cleanup/qA
Very important to be consistent across all samples in an experiment on how you size select your final libraries. You can size select by:
  Fragmenting your RNA, prior to cDNA generation.
    Chemically heat w/magnesium
    Mechanically (ex. ultra-sonicator)
Cleanup/Size select after library generation using SPRI beads or (gel cut)
QA the samples using an electrophoretic method (Bioanalyzer) and quantify with qPCR.
Most important thing is to be consistent!!!

## Slide 25: BE CONSISTANT!
In high throughput biological work (Microarrays, Sequencing, HT Genotyping, etc.), what may seem like small technical artifacts introduced during sample extraction/preparation can lead to large changes, or bias, in the data.
Not to say this doesn’t occur with smaller scale analysis such as Sanger sequencing or qRT-PCR, but they do become more apparent and may cause significant issues during analysis.

## Slide 26: WoRK Session 2
Perform
Search the internet for RNA-SEQ coverage recommendations. Then we will talk about them
RNA-SEQ COVERAGE

## Slide 27: RNA-seq pipeline overview

## Slide 28: Software
Preprocessing:
Python 2.7
  Modules: argparse, optparse, distutils
bowtie2 - contaminant screening
  http://bowtie-bio.sourceforge.net/bowtie2/index.shtml
Super-Deduper – Identify and remove PCR duplicates
  https://github.com/dstreett/Super-Deduper
Sickle – Trim low quality regions
  https://github.com/dstreett/sickle
Scythe – Identify and remove adapters in SE reads
  https://github.com/ucdavis-bioinformatics/scythe
FLASH2 – Join overlapping reads, identify and remove adapter in PE reads
  https://github.com/dstreett/FLASH2

## Slide 29: Software
Mapping:
Python 2.7
Bwa mem – map reads to a reference
  http://sourceforge.net/projects/bio-bwa/files/
samtools – processing of sam/bam file
  http://www.htslib.org/
Read Counting:
Python 2.7
samtools – processing of sam/bam file
  http://www.htslib.org/
HTeq-0.6.1 htseq_count – count reads occurrences within genes
  http://www-huber.embl.de/users/anders/HTSeq/

## Slide 30: Software
Analysis of differential expression:
R 3.2.0
  http://www.r-project.org/
  R Package: optparse from cran
  R Package: EdgeR from bioconductor – differential expression analysis
  http://bioconductor.org/packages/release/bioc/html/edgeR.html
Rstudio
  https://www.rstudio.com/

## Slide 31: Sequencing Read files

## Slide 32: Quality Scores

## Slide 33: Qscore Conversion

## Slide 34: Illumina Read naming conventions
CASAVA 1.8 Read IDs
@EAS139:136:FC706VJ:2:2104:15343:197393 1:Y:18:ATCACG
  EAS139 the unique instrument name 136 the run id
  FC706VJ the flowcell id 2 flowcell lane
  2104 tile number within the flowcell lane
  15343 ’x’-coordinate of the cluster within the tile
  197393 ’y’-coordinate of the cluster within the tile
  1 the member of a pair, 1 or 2 (paired-end or mate-pair reads only)
  Y Y if the read fails filter (read is bad), N otherwise
  18 0 when none of the control bits are on, otherwise it is an even number
  ATCACG index sequence

## Slide 35: The Command line
SECTION 3

## Slide 36: The command line
The command line is powerful and the preferred way to run bioinformatics tools
BASICS:
Prompt msettles@MacBook-Pro:~$
~ is your home director
... $ command [parameters] [files] ENTER
parameters begin with a - short parameter or -- long parameter
Help ... $ man command
… $ command –h
… $ command –help
Tab complete!!

## Slide 37: The command line
Command input/output:
file/folder on the command line, either as a positional argument or a parameter, or defaults
stdin aka ‘standard in’, input pipe
stdout aka ‘standard out’, output pipe
stderr aka ‘standard error’, pipe for error messages
Special characters:
| vertical bar is the pipe, it pipes the stdout of one command
to the stdin of another cmd
< > 2> feeds stdin, stdout, stderr to the command
>> append
& at the end of a command will run the command in the background
. Current directory
.. Up one folder
/ folder delimiter
* wild character, match anything
When naming files/folders avoid special characters and spaces ( use . and _ )!!

## Slide 38: The command line
Basics Commands:
pwd print the working directory (current dir)
ls [file/dir] list the current contents of the directory
ls –lah [file/dir] long list, human readable, show hidden of the directory
cd to change directory
cp f1 f2 copy file f1 to file f2
mv from to mv directory (also way to rename)
mkdir dir make directory
rm file remove file
rmdir dir remove an empty directory
rm –r dir recursively remove a non-empty directory
nano file edit a document
cat f1 [f2] print to stdout file f1 then if provided file f2 (concatenate)
less file view file, one page at a time
head file view the first 10 lines of a file
tail file view the last 10 lines of a file

## Slide 39: WoRK Session 1
Perform
Look at your home directory, what files are already there, what files are hidden
Create a new folder
Move into that folder and create a file (write anything)
Show that file, using less and cat
Go back to your home directory
Create a second folder
Copy the file from the first directory to the new directory
Move to your home directory
Remove both folders
Play with the new commands
Playing with the command line